Table of Contents
Work Log
Work todo
Documentation
SOAR
Bill of Materials
Assembly Instructions
Labs Completion Status
Design Labs
Software Labs
###### Work Log (since 1st meeting with Prof. Chuang)
Assembled a new hardware platform
Total = $231 ($169 without wireless) in quantity one
Debugged optical encoders ("3.3V" ones work when supplied at 5V…)
Debugged xbee wireless (don't use 115200, make sure to slowly read packets)
Head working (high current op-amp)
Documented our work
###### Work todo
- Enlarge (so that romeo controller can sit between motors) or add third layer to chassis: mount servo head and photodiode, mount full breadboard, mount IR sensors properly without velcro.
- Possibly roll our own board that
  - includes a 2 cell lipo charging circuit
  - is smaller
  - or a PCB chassis
  - add a piezo
  - Easily accessible on/off switches
- Otherwise, lasercut our chassis and IR sensor mounts possibly
- Order servos from factory
- Documentation
- GUI for pioneer to change the port
- Try out 300:1 motors
- A debugging stand (for lab 10 pet robot) -- currently wire spools
###### Documentation
###### SOAR
1. Replace /usr/local/lib/python2.7/dist-packages/soar/outputs/pioneer.py with our pioneer.py
2. Plug in xbee. In a terminal, run dmesg | tail -- it should say something like:
[41246.969987] usb 3-1: FTDI USB Serial Device converter now attached to ttyUSB0
1. sudo gedit /usr/local/lib/python2.7/dist-packages/soar/outputs/pioneer.py and change it to the right port for your connection, e.g.:
   settings.SERIAL_PORT_NAME = "/dev/ttyUSB0"
  1. If you want to see verbose output for debugging purposes, set debug = True
  2. If not, set debug = skip
2. Run soar
3. Click on Pioneer
  1. If should say P2OS Interface Ready and also denny: battery =
  2. If the button unclicks right away, probably your serial port is incorrect
4. Load a brain
5. Hit the run button
###### Bill of Materials

Name	Total Cost		Product Name	URL
Lasercut Chassis	7.95	pololu	#1507 Pololu 5" Robot Chassis RRC04A Transparent Light-Blue	http://www.pololu.com/product/1507
Lipo Battery Connector	0.99	pololu	JST RCY Plug with 10cm Leads, Male	http://www.pololu.com/product/2181
Lipo Battery	4.65	hobbyking	Turnigy 1000mAh 2S 20C Lipo Pack	http://www.hobbyking.com/hobbyking/store/__9170__Turnigy_1000mAh_2S_20C_Lipo_Pack.html
3x Sharp IR Sensor	29.85	pololu	#136 Sharp GP2Y0A21YK0F Analog Distance Sensor 10-80cm	http://www.pololu.com/product/136
3x Sharp IR mount	$15	robotmesh	Sharp IR Sensor Mounting Bracket-GP2Y0A21/GP2Y0A02YK	http://www.robotmesh.com/sharp-ir-sensor-mounting-bracket-gp2y0a21-gp2y0a02yk?___SID=U
2x 100:1 Gearmotor	33.9	pololu	#2214 100:1 Micro Metal Gearmotor HP with Extended Motor Shaft	http://www.pololu.com/product/2214
42x19mm Wheel, pair	3.85	robotmesh	Wheel 42x19mm (Pair)	http://www.robotmesh.com/wheel-42x19mm-pair
Extended Motor Bracket, Pair	2.99	pololu	#1089 Pololu Micro Metal Gearmotor Bracket Extended Pair	http://www.pololu.com/product/1089
2x Optical Encoder	17.9	pololu	#2591 Optical Encoder Pair Kit for Micro Metal Gearmotors, 3.3V	http://www.pololu.com/product/2591
2x Caster	$3.8	Robotmesh	MiniQ Ball Caster Metal	http://www.robotmesh.com/ball-caster-metal-miniq
3x Standoff	$2	Robotmesh	10 sets M3 * 30 nylon standoffs	http://www.robotmesh.com/10-sets-m3-30-nylon-standoffs
7x 3 wire	$6	Robotmesh	Analog Sensor Cable For Arduino (10 Pack)	http://www.robotmesh.com/analog-sensor-cable-for-arduino-10-pack
Romeo controller	$39.9	Robotmesh	Romeo V2-All in one Controller	http://www.robotmesh.com/romeo-v2-all-in-one-controller
Head Servo	$5	Emax / somewhere
			Subtotal	$168.78
Wireless
2x Xbee	41.9	Robotmesh	XBee 1mW Trace Antenna - Series 1 (802.15.4)	http://www.robotmesh.com/xbee-1mw-trace-antenna-series-1-802-15-4
Xbee USB adapter	18.5	Robotmesh	XBee USB Adapter V2	http://www.robotmesh.com/xbee-usb-adapter-v2
USB mini	1.9	Robotmesh	Mini USB cable	http://www.robotmesh.com/mini-usb-cable
			Total	$236.08

###### Assembly Instructions
See bill of materials for needed parts. Additionally, wire strippers and soldering iron needed.

Motor Unit Assembly
1. Solder optical encoder to gearmotor
2. Tune with oscilloscope and plastic screwdriver (see http://www.pololu.com/product/2590 for more details)
3. Put motor bracket on gearmotor
4. Put wheel on gearmotor

Sensor Unit Assembly
1. Screw IR sensor onto IR mount
2. Swap two wires by cutting, stripping, and soldering them, on the 3-wire analog connector

Servo Head Assembly (not needed in future)
1. Take off bottom part of case4121
2. Desolder control board
3. Resolder 3-wire leads to motor
4. Cut and strip a new 3-wire
5. Solder 3-wire leads to potentiometer
6. Place leads appropriately and put case back on
7. Future: photodiode mount and wiring, servo mount

Robot Assembly
1. Screw motor bracket down to chassis
2. Screw casters onto chassis
3. Screw standoffs to chassis
4. Screw romeo controller to standoffs

Program Xbees
1. Boot into windows and install XCTU
2. Program the xbees to talk to each other (DL and MY commands)
3. Set the baud rate to 19200

Robot Wiring
1. Cut and strip two leads on one of the 3-wires for the motor
2. Plug in / screw leads for motor to M1/M2 and digital pins
3. Plug in IR sensor to analog input pins
4. Plug in Xbee
5. Screw in JST 2-wire XH-style lipo male connector
6. Plug-in battery
###### Labs Completion Status
###### Design Labs
1. Wall Find done http://www.youtube.com/watch?v=qMBVbE07Tbg / Boundary Follow, bang bang http://www.youtube.com/watch?v=XguJQcxj43A (virtual)
2. x
3. n/a
4. x
5. x
6. Boundary Follow Error+Angle (requires re-implementing sonarDist, which relies on 8 sonar readings to calculate angle and distance), Bulls Eye
7. n/a
8. Head with potentiometer http://www.youtube.com/watch?v=5r9yhMpieDI (position control with motor pot and external pot shown)
9. Head with photodiode http://www.youtube.com/watch?v=XeEDuTtJMeo (mystery right now -- rails to one side if light is not applied)
10. Robot with head -- on hold due to railing of circuit, but seems to work fine
11. x
12. x
13. x
14. Maze
###### Software Labs
1. n/a
2. x
3. x
4. x
5. x
6. x
7. n/a
8. Head circuit
9. Head and robot
10. x
11. n/a
12. x
13. Parking
14. Maze